## Slide 1: Lecture 9 - Firewalls
IT&C 515R – Applications of Cybersecurity Training

## Slide 2: What is a Firewall?
A firewall is a network security system that monitors and controls incoming and outgoing network traffic based on security rules.
Key Functions:
  Blocks unauthorized access
  Filters traffic based on policies
  Logs and monitors traffic.

## Slide 3: Types of Firewalls
Host-Based Firewalls: Protect individual devices (e.g., Linux firewalls).
Network Firewalls: Protect entire networks (e.g., hardware appliances).
Packet-Filtering Firewalls: Analyze headers to allow or block traffic.
Stateful Firewalls: Track connection states for more advanced filtering.

## Slide 4: Linux Firewall Tools Overview
UFW (Uncomplicated Firewall): Simplified interface for iptables.
iptables: A low-level, rule-based packet filtering system.
Firewalld: A dynamic, modern firewall management tool.

## Slide 5: UFW
UFW is a user-friendly interface for managing iptables firewall rules
Designed to be easy to use, even for beginners.​
Default Deny Incoming
Default Allow Outgoing
Application Integration
New rules apply to new connections not exisiting

## Slide 6: Firewalld
firewalld is a dynamic firewall management tool for Linux systems
Zones: firewalld organizes rules into predefined zones such as public, internal, and external.
Rule Types
  Default Zone Rules​
  Service Rules
  Port Rules
  ICMP Rules
  Masquerade and Forwarding

## Slide 7: iptables
iptables allows users to filter and control network packets based on various criteria, including IP addresses, ports, and protocols.​
Rule Types:​
  Input Rules
  Output Rules
  Forward Rules

## Slide 8: Questions